## Slide 1
The work has been carried out with the financial support of the Ministry of Education and Science of the Russian Federation
(Agreement № 14.577.21.0242 on granting subsidies from 26.09.2017, the unique identifier of the project RFMEFI57717X0242).
UNIVERSAL MODULAR BOOSTER TRANSFORMER FOR MEDIUM VOLTAGE DISTRIBUTION NETWORKS
Global Invention Forum in Cyprus
October 14-15, 2020

## Slide 2
Transition to a Smart Grid system
operational power flows control in medium voltage distribution networks
structure management of medium voltage distribution networks
reduction in the cost of power supply for the end consumer
Universal modular booster transformer (UMBT)
Operating principle
SOLVED PROBLEM
TS
6-10/
0,4 kV
DDS
110/6-10 kV
DDS
110/6-10 kV
TS
6-10/
0,4 kV
TS
6-10/
0,4 kV
TS
6-10/
0,4 kV
UMBT1
6-10 kV
UMBT 2
6-10 kV
power flow direction and value change
Main power transmission lines
U>110 kV
Power distribution network
6-10 kV
Transversal voltage control
(voltage phase change)
Longitudinal voltage control
(voltage value change)
Active power flow change
Reactive power flow change

## Slide 3
Performed functions
Voltage regulation at distribution network nodes
Regulation of active and reactive power flows
Changing the configuration of the distribution network
Series
transformers
Electricity consumer
Shunt transformer
6 kV
6/0.4 kV
Control system
UMBT
Thyristor
switch
UNIVERSAL MODULAR BOOSTER TRANSFORMER (UMBT)
Parameter | Value
Nominal voltage (supply voltage) | 6 kV ±10%
Variation range of the angle voltage phase α | ± 5°
Measurement resolution of the phase shift voltage α | 1.5°
Range of regulation voltage | ± 10%
Regulation discreteness of the voltage amplitude | ≤ 1.5%
Load power | ≤ 630 кVA
Shunt-wound transformer power | 106 kVA
Series transformer power | 3×28 kVA
Technical characteristics of the UMBT
Intellectual property
Patent RU 2710886 (30.12.2019)

## Slide 4
Thyristor
switch
Shunt and series
transformers
High voltage switchgear
UNIVERSAL MODULAR BOOSTER TRANSFORMER PROTOTYPE

## Slide 5
POSITIVE IMPACT
COMPETITIVE ADVANTAGES
Stabilization of voltage level on consumer buses
Reduction of electrical losses in the network
Increasing the capacity of power lines
Load equalization of supply transformers
Improving the reliability of power supply
Connection without reconstruction of electrical networks
High-speed operation
Increased operational life
TVR
6-10 kV
Electricity consumer
DDS
110/6-10 kV
TS
6-10/
0,4 kV
Power transmission line
10 kV
Un+10%
Un-10%
Un-20%
Un
COMPETITIVE ADVANTAGES
Electric power complex enterprises
Industrial enterprises with a multi-level internal power supply system

## Slide 6
Electric Power Engineering, Power Supply and Power Electronics Department
Project Manager
DSc, professor Elena Sosnina
+79092872290, e-mail: sosnina@nntu.ru